## Slide 1: There are 3 types of rotation for Large Motor in EV3: +Turn motor through a given angle +Turn motor for a given time +Turn motor 'forever'

## Slide 2: Important to remember
DO NOT SET THE SPEED OF THE ROBOT TO OVER 900 OR -900

## Slide 3: Turn motor through a given angle

## Slide 4: Exericise 1:
Step 1: Make the robot go forward and rotate 720 degrees.
Step 2: Make the robot go backwards using -720 degrees
Step 3: Does the robot go backwards if you set speed_sp to a negative value and position_sp set to a positive value?

## Slide 5: Turn motor for a given time

## Slide 6: Exercise 2:
Step 1: Make the robot go forwards for 3 seconds and then go backwards for 2 seconds.
Step 2: Run the program from the command line (lift the robot up) and print out the actual speed of the robot (m.speed).
Step 3: What happens if time_sp is a negative value?

## Slide 7: Turn motor ‘forever’

## Slide 8: Exercise 3:
Step 1: Make the robot go straight using run_forever function for 3 seconds and stop for 1 second. Then go backwards for 3 seconds and stop.
Step 2: How many types do stop_action have? What are they? Hint: similar to Mindstorm
Step 3: Implement different stop_action

## Slide 9: Wait for completion

## Slide 10: Exercise 4:
Make the robot turn left 90 degrees. Then go straight for 2 seconds and turn right 90 degrees. Then finish the program with sys.exit().